## Slide 1: CSCI-351 Data communication and Networks
Lecture 11: Transport
(UDP, but mostly TCP)
The slide is built with the help of Prof. Alan Mislove, Christo Wilson, and David Choffnes's class

## Slide 2: Transport Layer
Function:
  Demultiplexing of data streams
Optional functions:
  Creating long lived connections
  Reliable, in-order packet delivery
  Error detection
  Flow and congestion control
Key challenges:
  Detecting and responding to congestion
  Balancing fairness against high utilization
Application
Presentation
Session
Transport
Network
Data Link
Physical
Notes: Flow vs. congestion
(receiver vs. sender)

## Slide 3: Outline
UDP
TCP
Congestion Control
Evolution of TCP
Problems with TCP

## Slide 4: The Case for Multiplexing
Datagram network
  No circuits
  No connections
Clients run many applications at the same time
  Who to deliver packets to?
Using IP header “protocol” field?
  8 bits = 256 concurrent streams
Insert Transport Layer to handle demultiplexing
Packet
Network
Data Link
Physical
Transport
Notes: IP protocol field has only 8 bits

## Slide 5: Demultiplexing Traffic
Endpoints identified by <src_ip, src_port, dest_ip, dest_port>
Network
Transport
Application
P1
P2
P3
P4
P6
P7
P5
Host 1
Host 2
Host 3
Unique port for each application
Server applications communicate with multiple clients

## Slide 6: Layering, Revisited
Application
Transport
Network
Data Link
Physical
Host 1
Router
Host 2
Physical
Lowest level end-to-end protocol (in theory)
  Transport header only read by source and destination
  Routers view transport header as payload
Application
Transport
Network
Data Link
Physical
Network
Data Link
Layers communicate peer-to-peer

## Slide 7: User Datagram Protocol (UDP)
Simple, connectionless datagram
  C sockets: SOCK_DGRAM
Port numbers enable demultiplexing
  16 bits = 65535 possible ports
  Port 0 is invalid
Checksum for error detection
  Detects (some) corrupt packets
  Does not detect dropped, duplicated, or reordered packets
Destination Port
0
16
31
Payload Length
Source Port
Checksum
Notes: UDP checksum is a the complement of a 16-bit one's complement sum

## Slide 8: Uses for UDP
Invented after TCP
  Why?
Not all applications can tolerate TCP
Custom protocols can be built on top of UDP
  Reliability? Strict ordering?
  Flow control? Congestion control?
Examples
  RTMP, real-time media streaming (e.g. voice, video)
  Facebook datacenter protocol
    Why?

## Slide 9: Outline
UDP
TCP
Congestion Control
Evolution of TCP
Problems with TCP

## Slide 10: Announcement
Class
Class by Prof. Kwon
No Class
Class

## Slide 11: Recap TCP (High-level concept)
Reliable Transmission
  3-ways handshake
  Sequence and acknowledgement number
    To make sure the receiver has received the packet
Flow control (Receiver-side)
Congestion control (Sender-side)

## Slide 12: Transmission Control Protocol
Options
Reliable, in-order, bi-directional byte streams
  Port numbers for demultiplexing
  Virtual circuits (connections)
  Flow control
  Congestion control, approximate fairness
Destination Port
0
16
31
Sequence Number
Source Port
Acknowledgement Number
Advertised Window
Urgent Pointer
Flags
Checksum
4
HLen

## Slide 13: Common TCP Options
Window scaling
SACK: selective acknowledgement
Maximum segment size (MSS)
Timestamp
Options
Destination Port
0
16
31
Sequence Number
Source Port
Acknowledgement Number
Advertised Window
Urgent Pointer
Flags
Checksum
4
HLen

## Slide 14: Connection Setup
Why do we need connection setup?
  To establish state on both hosts
  Most important state: sequence numbers
    Count the number of bytes that have been sent
    Initial value chosen at random
    Why?
Important TCP flags (1 bit each)
  SYN – synchronization, used for connection setup
  ACK – acknowledge received data
  FIN – finish, used to tear down connection
Notes: it is possible that two communicating hosts are using the same port number that is used in the past

## Slide 15: Three Way Handshake
Each side:
  Notifies the other of starting sequence number
  ACKs the other side’s starting sequence number
Client
Server
SYN <SeqC, 0>
SYN/ACK <SeqS, SeqC+1>
ACK <SeqC+1, SeqS+1>
Why
Sequence # +1?
Notes: 211

## Slide 16: Connection Setup Issues
Connection confusion
  How to disambiguate connections from the same host?
  Random sequence numbers
Source spoofing
  Need good random number generators!
Connection state management
  Each SYN allocates state on the server
  SYN flood = denial of service attack
  Solution: SYN cookies
Notes: Spoofing + sequence prediction to hijack connections
32bits: timestamp, MSS, 4 tuples
Top 5bits: t mod 32
Middle 3 bits: MSS (maximum segment size)
Bottom 24 bits: hash functions of (ip, port, ip, port)

## Slide 17: Connection Tear Down
Either side can initiate tear down
Other side may continue sending data
  Half open connection
Acknowledge the last FIN
  Sequence number + 1
Client
Server
FIN <SeqA, *>
ACK <*, SeqA+1>
ACK
Data
FIN <SeqB, *>
ACK <*, SeqB+1>

## Slide 18: Sequence Number Space
TCP uses a byte stream abstraction
  Each byte in each stream is numbered
  32-bit value, wraps around
  Initial, random values selected during setup
Byte stream broken down into segments (packets)
  Size limited by the Maximum Segment Size (MSS)
  Set to limit fragmentation
Each segment has a sequence number
Segment 8
Segment 9
Segment 10
13450
14950
16050
17550
Notes: MSS: 1500 where MTU size, but it’s not practical here
Min IP header: 20 bytes
Min tcp header: 20 bytes
so, MSS: 1500 - 20 - 20

## Slide 19: Bidirectional Communication
Each side of the connection can send and receive
  Different sequence numbers for each direction
Client
Server
Data (1460 bytes)
Data/ACK (730 bytes)
Data/ACK (1460 bytes)
Seq.
Ack.
Seq.
Ack.
1
23
23
1461
1461
753
753
2921
Data and ACK in the same packet
23
1

## Slide 20: Flow Control
Problem: how many packets should a sender transmit?
  Too many packets may overwhelm the receiver
  Size of the receivers buffers may change over time
Solution: sliding window
  Receiver tells the sender how big their buffer is
  Called the advertised window
  For window size n, sender may transmit n bytes without receiving an ACK
  After each ACK, the window slides forward
Window may go to zero!

## Slide 21: Flow Control: Sender Side
Sequence Number
Src. Port
Acknowledgement Number
Window
Urgent Pointer
Flags
Checksum
HL
Packet Sent
Dest. Port
Src. Port
Acknowledgement Number
Window
Urgent Pointer
Flags
Checksum
HL
Packet Received
Dest. Port
Sequence Number
ACKed
Sent
To Be Sent
Outside Window
Window
App Write
Must be buffered until ACKed
Notes: Each side acts and sender and receiver
Every message contains sequence number, even if payload length is zero
Every message contains acknowledgements, even if no data was received
Every message advertises the window size

## Slide 22: Sliding Window Example
1
2
3
4
5
6
7
5
6
7
Time
Time
TCP is ACK Clocked
Short RTT  quick ACK  window slides quickly
Long RTT  slow ACK  window slides slowly

## Slide 23: What Should the Receiver ACK?
ACK every packet
Use cumulative ACK, where an ACK for sequence n implies ACKS for all k < n
Use negative ACKs (NACKs), indicating which packet did not arrive
Use selective ACKs (SACKs), indicating those that did arrive, even if not in order
  SACK is an actual TCP extension
20

## Slide 24: Sequence Numbers, Revisited
32 bits, unsigned
Guard against stray packets
  IP packets have a maximum segment lifetime (MSL) of 120 seconds
    i.e. a packet can linger in the network for 2 minutes
  Sequence number would wrap around

## Slide 25: Silly Window Syndrome
Problem: what if the window size is very small?
  Multiple, small packets, headers dominate data
Equivalent problem: sender transmits packets one byte at a time
for (int x = 0; x < strlen(data); ++x)
write(socket, data + x, 1);
Header
Data
Header
Data
Header
Data
Header
Data
Notes: TCP vs. UDP
Widow size vs. data size.

## Slide 26: Nagle’s Algorithm
If the window >= MSS and available data >= MSS:
  Send the data
Elif there is unACKed data:
  Enqueue data in a buffer (send after a timeout)
Else: send the data
Problem: Nagle’s Algorithm delays transmissions
  What if you need to send a packet immediately?
  int flag = 1;
  setsockopt(sock, IPPROTO_TCP, TCP_NODELAY, (char *) &flag, sizeof(int));
Send a full packet
Send a non-full packet if nothing else is happening
Notes: Used to be useful. When the bandwidth resource is very scarce

## Slide 27: Error Detection
Checksum detects (some) packet corruption
  Computed over IP header, TCP header, and data
Sequence numbers catch sequence problems
  Duplicates are ignored
  Out-of-order packets are reordered or dropped
  Missing sequence numbers indicate lost packets
Lost segments detected by sender
  Use timeout to detect missing ACKs
  Need to estimate RTT to calibrate the timeout
  Sender must keep copies of all data until ACK

## Slide 28: Retransmission Time Outs (RTO)
Problem: time-out is linked to round trip time
Initial Send
ACK
Retry
RTO
Initial Send
ACK
Retry
RTO
Timeout is too short
What about if timeout is too long?

## Slide 29: Round Trip Time Estimation
Original TCP round-trip estimator
  RTT estimated as a moving average
  new_rtt = α (old_rtt) + (1 – α)(new_sample)
  Recommended α: 0.8-0.9 (0.875 for most TCPs)
RTO = 2 * new_rtt (i.e. TCP is conservative)
Data
ACK
Sample

## Slide 30: RTT Sample Ambiguity
Karn’s algorithm: ignore samples for retransmitted segments
Initial Send
ACK
Retry
RTO
Initial Send
ACK
Retry
RTO
Sample
Sample?

## Slide 31: Outline
UDP
TCP
Flow Control
Congestion Control
Evolution of TCP
Problems with TCP

## Slide 32: What is Congestion?
Load on the network is higher than capacity
  Capacity is not uniform across networks
    Modem vs. Cellular vs. Cable vs. Fiber Optics
  There are multiple flows competing for bandwidth
    Residential cable modem vs. corporate datacenter
  Load is not uniform over time
    10pm, Sunday night = Bittorrent Game of Thrones

## Slide 33: Why is Congestion Bad?
Results in packet loss
  Routers have finite buffers
  Internet traffic is self similar, no buffer can prevent all drops
  When routers get overloaded, packets will be dropped
Practical consequences
  Router queues build up, delay increases
  Wasted bandwidth from retransmissions
  Low network goodput

## Slide 34: The Danger of Increasing Load
Knee – point after which
  Throughput increases very slow
  Delay increases fast
Cliff – point after which
  Throughput  0
  Delay  ∞
Congestion Collapse
Load
Load
Goodput
Delay
Knee
Cliff
Ideal point

## Slide 35: Cong. Control vs. Cong. Avoidance
Congestion Collapse
Goodput
Knee
Cliff
Load
Congestion Avoidance:
Stay left of the knee
Congestion Control:
Stay left of the cliff

## Slide 36: Advertised Window, Revisited
Does TCP’s advertised window solve congestion?
NO
The advertised window only protects the receiver
A sufficiently fast receiver can max the window
  What if the network is slower than the receiver?
  What if there are other concurrent flows?
Key points
  Window size determines send rate
  Window must be adjusted to prevent congestion collapse

## Slide 37: Goals of Congestion Control
Adjusting to the bottleneck bandwidth
Adjusting to variations in bandwidth
Sharing bandwidth between flows
Maximizing throughput

## Slide 38: General Approaches
Do nothing, send packets indiscriminately
  Many packets will drop, totally unpredictable performance
  May lead to congestion collapse
Reservations
  Pre-arrange bandwidth allocations for flows
  Requires negotiation before sending packets
  Must be supported by the network
Dynamic adjustment
  Use probes to estimate level of congestion
  Speed up when congestion is low
  Slow down when congestion increases
  Messy dynamics, requires distributed coordination

## Slide 39: TCP Congestion Control
Each TCP connection has a window
  Controls the number of unACKed packets
Sending rate is ~ window/RTT
Idea: vary the window size to control the send rate
Introduce a congestion window at the sender
  Congestion control is sender-side problem

## Slide 40: Congestion Window (cwnd)
Limits how much data is in transit
Denominated in bytes
wnd = min(cwnd, adv_wnd);
effective_wnd = wnd –
(last_byte_sent – last_byte_acked);
last_byte_acked
last_byte_sent
wnd
effective_wnd

## Slide 41: Two Basic Components
Detect congestion
  Packet dropping is most reliably signal
    Delay-based methods are hard and risky
  How do you detect packet drops? ACKs
    Timeout after not receiving an ACK
    Several duplicate ACKs in a row (ignore for now)
Rate adjustment algorithm
  Modify cwnd
  Probe for bandwidth
  Responding to congestion

## Slide 42: Rate Adjustment
Recall: TCP is ACK clocked
  Congestion = delay = long wait between ACKs
  No congestion = low delay = ACKs arrive quickly
Basic algorithm
  Upon receipt of ACK: increase cwnd
    Data was delivered, perhaps we can send faster
    cwnd growth is proportional to RTT
  On loss: decrease cwnd
    Data is being lost, there must be congestion
Question: increase/decrease functions to use?

## Slide 43: Utilization and Fairness
Flow 1 Throughput
Flow 2 Throughput
Max throughput for flow 2
Zero throughput for flow 1
Max throughput for flow 1
Zero throughput for flow 2
Less than full utilization
More than full utilization (congestion)
Ideal point
Max efficiency
Perfect fairness
Equal throughput
(fairness)

## Slide 44: Multiplicative Increase, Additive Decrease
Not stable!
Veers away from fairness
Flow 1 Throughput
Flow 2 Throughput

## Slide 45: Additive Increase, Additive Decrease
Stable
But does not converge to fairness
Flow 1 Throughput
Flow 2 Throughput

## Slide 46: Multiplicative Increase, Multiplicative Decrease
Stable
But does not converge to fairness
Flow 1 Throughput
Flow 2 Throughput

## Slide 47: Additive Increase, Multiplicative Decrease
Converges to stable and fair cycle
Symmetric around y=x
Flow 1 Throughput
Flow 2 Throughput

## Slide 48: Implementing Congestion Control
Maintains three variables:
  cwnd: congestion window
  adv_wnd: receiver advertised window
  ssthresh: threshold size (used to update cwnd)
For sending, use: wnd = min(cwnd, adv_wnd)
Two phases of congestion control
  Slow start (cwnd < ssthresh)
    Probe for bottleneck bandwidth
  Congestion avoidance (cwnd >= ssthresh)
    AIMD
45

## Slide 49: Slow Start
Goal: reach knee quickly
Upon starting (or restarting) a connection
  cwnd =1
  ssthresh = adv_wnd
  Each time a segment is ACKed, cwnd++
Continues until…
  ssthresh is reached
  Or a packet is lost
Slow Start is not actually slow
  cwnd increases exponentially
Load
Goodput
Knee
Cliff

## Slide 50: Slow Start Example
1
2
3
4
5
6
7
cwnd = 1
cwnd = 2
cwnd = 4
cwnd = 8
cwnd grows rapidly
Slows down when…
  cwnd >= ssthresh
  Or a packet drops

## Slide 51: Congestion Avoidance
AIMD mode
ssthresh is lower-bound guess about location of the knee
If cwnd >= ssthresh then each time a segment is ACKed increment cwnd by 1/cwnd (cwnd += 1/cwnd).
So cwnd is increased by one only if all segments have been acknowledged

## Slide 52: Congestion Avoidance Example
Chart: 
| t=0 | t=1 | t=2 | t=3 | t=4 | t=5 | t=6 | t=7
Cwnd | 1 | 2 | 4 | 8 | 9 | 10 | 11 | 12
Round Trip Times
cwnd (in segments)
Slow Start
cwnd >= ssthresh
cwnd = 1
cwnd = 2
cwnd = 4
cwnd = 8
cwnd = 9
ssthresh = 8

## Slide 53: TCP Pseudocode
Initially: cwnd = 1; ssthresh = adv_wnd;
New ack received: if (cwnd < ssthresh) /* Slow Start*/ cwnd = cwnd + 1; else /* Congestion Avoidance */ cwnd = cwnd + 1/cwnd;
Timeout: /* Multiplicative decrease */ ssthresh = cwnd/2; cwnd = 1;

## Slide 54: The Big Picture
Time
cwnd
Timeout
Slow Start
Congestion
Avoidance
ssthresh

## Slide 55: Outline
UDP
TCP
Congestion Control
Evolution of TCP
Problems with TCP

## Slide 56: The Evolution of TCP
Thus far, we have discussed TCP Tahoe
  Original version of TCP
However, TCP was invented in 1974!
  Today, there are many variants of TCP
Early, popular variant: TCP Reno
  Tahoe features, plus…
  Fast retransmit
  Fast recovery

## Slide 57: TCP Reno: Fast Retransmit
Reno: retransmit after 3 duplicate ACKs
1
2
3
4
5
6
7
cwnd = 1
cwnd = 2
cwnd = 4
2
3
4
4
4
4
3 Duplicate ACKs
Notes: Without FRR, the TCP uses a timer that requires a retransmission timeout if a packet is lost. No new or duplicate packets can be sent during the timeout period.

## Slide 58: The Big Picture
Time
cwnd
3 DUPACKs
Slow Start
Congestion
Avoidance
ssthresh
Timeout

## Slide 59: TCP Reno: Fast Recovery
After a fast-retransmit set cwnd & ssthresh to cwnd/2
  i.e. don’t reset cwnd to 1
  Avoid unnecessary return to slow start
  Prevents expensive timeouts
But when RTO expires still do cwnd = 1
  Return to slow start
  Indicates packets aren’t being delivered at all
  i.e. congestion must be really bad

## Slide 60: Fast Retransmit and Fast Recovery
At steady state, cwnd oscillates around the optimal window size
TCP always forces packet drops
Time
cwnd
Timeout
Slow Start
Congestion Avoidance
Fast Retransmit/Recovery
ssthresh
Timeout

## Slide 61: Many TCP Variants…
Tahoe: the original
  Slow start with AIMD
  Dynamic RTO based on RTT estimate
Reno: fast retransmit and fast recovery
NewReno: improved fast retransmit
  Each duplicate ACK triggers a retransmission
  Problem: >3 out-of-order packets causes pathological retransmissions
Vegas: delay-based congestion avoidance
And many, many, many more…

## Slide 62: Common TCP Options
Window scaling
SACK: selective acknowledgement
Maximum segment size (MSS)
Timestamp
Options
Destination Port
0
16
31
Sequence Number
Source Port
Acknowledgement Number
Advertised Window
Urgent Pointer
Flags
Checksum
4
HLen

## Slide 63: SACK: Selective Acknowledgment
Problem: duplicate ACKs only tell us about 1 missing packet
  Multiple rounds of dup ACKs needed to fill all holes
Solution: selective ACK
  Include received, out-of-order sequence numbers in TCP header
  Explicitly tells the sender about holes in the sequence
8
9
10
11
4
4
5
6
7
4
4
4
4

## Slide 64: Other Common Options
Maximum segment size (MSS)
  Essentially, what is the hosts MTU
  Saves on path discovery overhead
Timestamp
  When was the packet sent (approximately)?
  Used to prevent sequence number wraparound

## Slide 65: Issues with TCP
The vast majority of Internet traffic is TCP
However, many issues with the protocol
  Lack of fairness
  Poor performance with small flows
  Really poor performance on wireless networks
  Susceptibility to denial of service

## Slide 66: SYN Cookies
Did the client really send me a SYN recently?
  Timestamp: freshness check
  Cryptographic hash: prevents spoofed packets
Maximum segment size (MSS)
  Usually stated by the client during initial SYN
  Server should store this value…
  Reflect the clients value back through them
Sequence Number
Timestamp
31
0
5
MSS
8
Hash of two end-points’ IP & Port
Notes: let t be a slowly incrementing timestamp (typically time() logically right-shifted 6 positions, which gives a resolution of 64 seconds)
let m be the maximum segment size (MSS) value that the server would have stored in the SYN queue entry
let s be the result of a cryptographic hash function computed over the server IP address and port number, the client IP address and port number, and the value t. The returned value s must be a 24-bit value.
> Firstly, the server is limited to only 8 unique MSS values, as that is all that can be encoded in 3 bits. Secondly, the server must reject all TCP options (such as large windows or timestamps), because the server discards the SYN queue entry where that information would otherwise be stored.[1]

## Slide 67: SYN Cookies in Practice
Advantages
  Effective at mitigating SYN floods
  Compatible with all TCP versions
  Only need to modify the server
  No need for client support
Disadvantages
  MSS limited to 3 bits, may be smaller than clients actual MSS
  Server forgets all other TCP options included with the client’s SYN
    SACK support, window scaling, etc.