## Slide 1: Comments about the quiz?
No limit of challenges;
  But you need to bring a document
  Still need to come to office hours with the following in writing:
    Specify the problem(s) you want regraded
    For each problem, explain why the grade is in error

## Slide 2: CSCI-351 Data communication and Networks
Lecture 12: DNS and your Project2
The slide is built with the help of Prof. Alan Mislove, Christo Wilson, and David Choffnes's class

## Slide 3: Why Skipping Transport Layer?
No; we will cover at the next class
Project 2 is announced: DNS
Application
Transport
Network
Data Link
Physical

## Slide 4: Project 2

## Slide 5: Project 2

## Slide 6: The IPv4 Shortage
Problem: consumer ISPs typically only give one IP address per-household
  Additional IPs cost extra
  More IPs may not be available
NAT and DHCP
  NAT + DHCP
Notes: Network Address Translator

## Slide 7: Basic NAT Operation
Private Network
Internet
Source: 192.168.0.1
Dest: 74.125.228.67
Source: 66.31.210.69
Dest: 74.125.228.67
66.31.210.69
Source: 74.125.228.67
Dest: 66.31.210.69
74.125.228.67
192.168.0.1
Source: 74.125.228.67
Dest: 192.168.0.1
Private Address | Public Address
192.168.0.1:2345 | 74.125.228.67:80

## Slide 8: Port-forwarding

## Slide 9: DHCP: Dynamic Host Configuration Protocol
Let’s say that a ISP has X customers, How many IPs does it need to have?
  X?
Goal: allow host to dynamically obtain its IP address from network server when it joins network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/“on”)
  support for mobile users who want to join network (more shortly)

## Slide 10: DHCP Client-Server

## Slide 11: DHCP Client-Server
DHCP server: 223.1.2.5
arriving
client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!
Notes: Your IP address

## Slide 12: DHCP: More than IP address
DHCP can return more than just allocated IP address on subnet
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 13: DHCP Header (Do not memorize)

## Slide 14: CSCI-351 Data communication and Networks
Lecture 12: DNS
The slide is built with the help of Prof. Alan Mislove, Christo Wilson, and David Choffnes's class

## Slide 15: Layer 8 (The Carbon-based nodes)
If you want to…
  Call someone, you need to ask for their phone number
    You can’t just dial “P R O F C H U N G”
  Mail someone, you need to get their address first
What about the Internet?
  If you need to reach Google, you need their IP
  Does anyone know Google’s IP?
Problem:
  People can’t remember IP addresses
  Need human readable names that map to IPs

## Slide 16: Internet Names and Addresses
Addresses, e.g. 129.10.117.100
  Computer usable labels for machines
  Conform to structure of the network
Names, e.g. www.rit.edu
  Human usable labels for machines
  Conform to organizational structure
How do you map from one to the other?
  Domain Name System (DNS)

## Slide 17: History
Before DNS, all mappings were in hosts.txt
  /etc/hosts on Linux
  C:\Windows\System32\drivers\etc\hosts on Windows
Centralized, manual system
  Changes were submitted to SRI via email
  Machines periodically FTP new copies of hosts.txt
  Administrators could pick names at their discretion
  Any name was allowed
    tijay_server_at_rit_pwns_joo_lol_kthxbye
Notes: SRI – Standford Research Institute

## Slide 18: Towards DNS
Eventually, the hosts.txt system fell apart
  Not scalable, SRI couldn’t handle the load
  Hard to enforce uniqueness of names
    e.g RIT
      Rochester Institute of Technology?
      Revolution in Training (US Navy)
  Many machines had inaccurate copies of hosts.txt
Thus, DNS was born

## Slide 19: Outline
DNS Basics
DNS Security

## Slide 20: DNS at a High-Level
Domain Name System
Distributed database
  No centralization
Simple client/server architecture
  UDP port 53, some implementations also use TCP
  Why? (You will learn at the TCP-lecture)
Hierarchical namespace
  As opposed to original, flat namespace
  e.g. .com  google.com  mail.google.com

## Slide 21: Naming Hierarchy
Top Level Domains (TLDs) are at the top
Maximum tree depth: 128
Each Domain Name is a subtree
  .edu  rit.edu  cs.rit.edu  www.ccs.rit.edu
Name collisions are avoided
  rit.edu vs. rit.com
Root
edu
com
gov
mil
org
net
uk
fr
etc.
rit
mit
cs
csec
gccis
www
login
mail

## Slide 22: Hierarchical Administration
Tree is divided into zones
  Each zone has an administrator
  Responsible for the part of the hierarchy
Example:
  cs controls *.cs.rit.edu
  RIT controls *.rit.edu
Root
edu
com
gov
mil
org
net
uk
fr
etc.
rit
mit
cs
www
login
mail
ICANN
Verisign

## Slide 23: Server Hierarchy
Functions of each DNS server:
  Authority over a portion of the hierarchy
    No need to store all DNS names
  Store all the records for hosts/domains in its zone
    May be replicated for robustness
  Know the addresses of the root servers
    Resolve queries for unknown names
Root servers know about all TLDs
  The buck stops at the root servers

## Slide 24: Root Name Servers
Responsible for the Root Zone File
  Lists the TLDs and who controls them
  ~272KB in size
com. 172800 IN NS a.gtld-servers.net.
com. 172800 IN NS b.gtld-servers.net.
com. 172800 IN NS c.gtld-servers.net.
Administered by ICANN
  13 root servers, labeled AM
  6 are anycasted, i.e. they are globally replicated
Contacted when names cannot be resolved
  In practice, most systems cache this information

## Slide 25: Map of the Roots (root-servers.org)

## Slide 26: Local Name Servers (Resolvers)
RIT
Each ISP/company has a local, default name server
Often configured via DHCP
Hosts begin DNS queries by contacting the local name server
Frequently cache query results
Where is google.com?

## Slide 27: Authoritative Name Servers
Stores the nameIP mapping for a given host
RIT
Where is www.rit.edu?
Root
edu
rit
www.rit.edu
Authority for ‘rit.edu’
www.rit.edu = 129.21.1.40
Authority for ‘edu’

## Slide 28: Basic Domain Name Resolution
Every host knows a local DNS server
  Sends all queries to the local DNS server
If the local DNS can answer the query, then you’re done
  Local server has cached the record for that name
Otherwise, go down the hierarchy and search for the authoritative name server
  Every local DNS server knows the root servers
  Use cache to skip steps if possible
    e.g. skip the root and go directly to .edu if the root file is cached

## Slide 29: Recursive DNS Query
Puts the burden of resolution on the contacted name server
How does glados know who to forward responses too?
  Random IDs embedded in DNS queries
What have we said about keeping state in the network?
Root
com
ns1.google.com
www.google.com
glados.cs.rit.edu
Where is www.google.com?

## Slide 30: Iterated DNS query
Contact server replies with the name of the next authority in the hierarchy
“I don’t know this name, but this other server might”
This is how DNS works today
Root
com
ns1.google.com
www.google.com
asgard.ccs.rit.edu
Where is www.google.com?

## Slide 31: DNS Propagation
How many of you have purchased a domain name?
  Did you notice that it took ~72 hours for your name to become accessible?
  This delay is called DNS Propagation
Root
com
ns.godaddy.com
www.my-new-site.com
asgard.ccs.rit.edu

## Slide 32: Caching vs. Freshness
DNS Propagation delay is caused by caching
asgard.ccs.rit.edu
Cached Root Zone File
Cached .com Zone File
Cached .net Zone File
Etc.
Root
com
ns.godaddy.com
www.my-new-site.com
Where is
www.my-new-site.com?
That name does not exist.
Zone files may be cached for 1-72 hours

## Slide 33: DNS Resource Records
DNS queries have two fields: name and type
Resource record is the response to a query
  Four fields: (name, value, type, TTL)
  There may be multiple records returned for one query
What are do the name and value mean?
  Depends on the type of query and response

## Slide 34: DNS Types
Type = NS
  Name = partial domain
  Value = name of DNS server for this domain
  “Go send your query to this other server”
Type = A / AAAA
  Name = domain name
  Value = IP address
  A is IPv4, AAAA is IPv6
Query
Name: www.rit.edu
Type: A
Resp.
Name: www.rit.edu
Value: 129.10.116.81
Query
Name: rit.edu
Type: NS
Resp.
Name: rit.edu
Value: ns1a.rit.edu.

## Slide 35: DNS Types, Continued
Type = CNAME
  Name = hostname
  Value = canonical hostname
  Useful for aliasing
  CDNs use this (will be covered)
Type = MX
  Name = domain in email address
  Value = canonical name of mail server
Query
Name: foo.mysite.com
Type: CNAME
Resp.
Name: foo.mysite.com
Value: bar.mysite.com
Query
Name: cs.rit.edu
Type: MX
Resp.
Name: cs.rit.edu
Value: pony-express.cs.rit.edu.

## Slide 36: Reverse Lookups
What about the IPname mapping?
Separate server hierarchy stores reverse mappings
  Rooted at in-addr.arpa and ip6.arpa
Additional DNS record type: PTR
  Name = IP address
  Value = domain name
Not guaranteed to exist for all IPs
Why do we need this?
Query
Name: 129.10.116.51 Type: PTR
Resp.
Name: 129.21.30.104
Value: cs.rit.edu

## Slide 37: Quiz Recap

## Slide 38: Announcements (1)
Project 1 scores….

## Slide 39: Announcements (2)
Project 2: You may use other languages than C
  MUST include a script that compiles or runs
    runme.sh which creates executable 351dns
  No third party libraries (of course, no dns-related libraries)
  Today’s is the due of the team registration

## Slide 40: Announcements (3)
No class at 10/09
Midterm reviews at 10/11
  Study hard and bring your questions

## Slide 41: Midterm
1 hour and 15 minutes
Closed book, closed notes, phones off
No need for calculator, no need to write working code
  You may be asked to write pseudocode
  You will be asked to write complete sentences

## Slide 42: DNS Recap (Big picture)
Name hierarchy
Two kinds of DNS servers:
  Authoritative Nameserver
  Resolver

## Slide 43: Naming Hierarchy
Top Level Domains (TLDs) are at the top
Maximum tree depth: 128
Each Domain Name is a subtree
  .edu  rit.edu  cs.rit.edu  www.ccs.rit.edu
Name collisions are avoided
  rit.edu vs. rit.com
Root
edu
com
gov
mil
org
net
uk
fr
etc.
rit
mit
cs
csec
gccis
www
login
mail

## Slide 44: Authoritative Nameserver
ns1a.rit.edu
What is the IP address of rit.edu?
What is the mail server address of rit.edu?
Do you have other names than rit.edu?
What is your IPv6 address?

## Slide 45: Process to look-up www.rit.edu
ns1a.rit.edu
a.edu-servers.net
. (root)
IP address of rit.edu?
I need .edu authoritative nameserver
a.edu-servers.net. and 192.5.6.30
I need rit.edu nameserver
a.edu-servers.net. and 192.5.6.30
IP of www.rit.edu
129.21.1.40

## Slide 46: Demo 1
Dig: (Domain Information Grouper)
  Very useful tool to send a DNS request and parse the DNS response

## Slide 47: Resolver
Contact server replies with the name of the next authority in the hierarchy
“I don’t know this name, but this other server might”
This is how DNS works today
Cache!
Root
com
ns1.google.com
www.google.com
asgard.ccs.rit.edu
Where is www.google.com?

## Slide 48: Demo 2
Dig: (Domain Information Grouper)
  Dig @1.1.1.1 rit.edu
  Dig @8.8.8.8 rit.edu

## Slide 49: DNS Types
Type = NS
  Name = partial domain
  Value = name of DNS server for this domain
  “Go send your query to this other server”
Type = A / AAAA
  Name = domain name
  Value = IP address
  A is IPv4, AAAA is IPv6
Query
Name: www.rit.edu
Type: A
Resp.
Name: www.rit.edu
Value: 129.10.116.81
Query
Name: rit.edu
Type: NS
Resp.
Name: rit.edu
Value: ns1a.rit.edu.

## Slide 51: How to buy a domain name (1)
.COM
(Verisign)
Registry
(TLD)
GoDaddy
Registrar
Owner
Buy
example.com
I need a domain
. (Root)
IANA
Makes TLDs (Top level domains)
You have authority to sell .com SLD domains
.com’s authoritative nameserver
You have authority to sell .com SLD domains

## Slide 52: How to buy a domain name (2) Using your own authoritative nameserver
.COM
(Verisign)
Registry
(TLD)
GoDaddy
Registrar
Owner
Buy
example.com
NS Record
I need a domain
.com’s authoritative nameserver
My nameserver name is ns.example.com and
this is the IP addresss: 1.2.3.4.
example.com NS ns.example.com
ns.example.com A 1.2.3.4
www.example.com A 9.9.9.9

## Slide 53: How to buy a domain name (3) Using the registrar’s default nameserver
.COM
(Verisign)
Registry
(TLD)
GoDaddy
Registrar
Owner
Buy
example.com
I need a domain
.com’s authoritative nameserver
example.com NS ns.godaddy.com
…
ns.godaddy.com A 4.5.6.7 (already here)
My webserver
IP addresss is 9.9.9.9
NS Record
Internally add
example.com A 9.9.9.9
example.com NS ns.godaddy.com

## Slide 54: DNS as Indirection Service
DNS gives us very powerful capabilities
  Not only easier for humans to reference machines!
Changing the IPs of machines becomes trivial
  e.g. you want to move your web server to a new host
  Just change the DNS record!

## Slide 55: Aliasing and Load Balancing
One machine can have many aliases (virtual hosting)
www.reddit.com
www.foursquare.com
www.huffingtonpost.com
*.blogspot.com
taejoong.github.io
cs.rit.edu/~tjc
One domain can map to multiple machines
www.google.com

## Slide 56: Content Delivery Networks
DNS responses may vary based on geography, ISP, etc
(details will be covered)

## Slide 57: Outline
DNS Basics
DNS Security

## Slide 58: The Importance of DNS
Without DNS…
  How could you get to any websites?
You are your mailserver
  When you sign up for websites, you use your email address
  What if someone hijacks the DNS for your mail server?
DNS is the root of trust for the web
  When a user types www.bankofamerica.com, they expect to be taken to their bank’s website
  What if the DNS record is compromised?

## Slide 59: Denial Of Service
Flood DNS servers with requests until they fail
October 2002: massive DDoS against the root name servers
  What was the effect?
  … users didn’t even notice
  Root zone file is cached almost everywhere
More targeted attacks can be effective
  Local DNS server  cannot access DNS
  Authoritative server  cannot access domain

## Slide 60: DNS Hijacking
Infect their OS or browser with a virus/trojan
  e.g. Many trojans change entries in /etc/hosts
  *.bankofamerica.com  evilbank.com
Man-in-the-middle
Response Spoofing
  Eavesdrop on requests
  Outrace the servers response

## Slide 61: DNS Spoofing
dns.bofa.com
123.45.67.89
Where is bankofamerica.com?
dns.evil.com
66.66.66.93
123.45.67.89
Where is bankofamerica.com?
How do you know that a given nameIP mapping is correct?
66.66.66.93

## Slide 62: DNS Cache Poisoning
Until the TTL expires, all queries for BofA to dns.rit.edu will return poisoned result
Much worse than spoofing/man-in-the-middle
  Whole ISPs can be impacted!
ns1.google.com
dns.rit.edu
Where is www.google.com?
www.google.com = 74.125.131.26
bankofamerica.com = 66.66.66.92
Where is bankofamerica.com?

## Slide 63: DNS Header
Query identifier:
used to be incremented by 1

## Slide 64: Attacking DNS (only few examples)
Kaminsky Attack
(QID bruteforcing)
Random QID and
Random Port
Man-in-the-Middle
?
?

## Slide 65: Solution: DNSSEC (Will be detailed)
Cryptographically sign critical resource records
  Resolver can verify the cryptographic signature
Two new resource types
  Type = DNSKEY
    Name = Zone domain name
    Value = Public key for the zone
  Type = RRSIG
    Name = (type, name) tuple, i.e. the query itself
    Value = Cryptographic signature of the query results
Deployment
  On the roots since July 2010
  Verisign enabled it on .com and .net in January 2011
  Comcast is the first major ISP to support it (January 2012)
Prevents hijacking and spoofing
Creates a hierarchy of trust within each zone

## Slide 66: DNSSEC Hierarchy of Trust
dns.bofa.com
Where is bankofamerica.com?
IP: 123.45.67.89
Key: < >
SIG: x9fnskflkalk
.com (Verisign)
Root Zone (ICANN)
dns.evil.com
IP: 66.66.66.93
Key: < >
SIG: 9na8x7040a3

## Slide 67: Site Finder
September 2003: Verisign created DNS wildcards for *.com and *.net
  Essentially, catch-all records for unknown domains
  Pointed to a search website run by Verisign
  Search website was full of advertisements
Extremely controversial move
  Is this DNS hijacking?
  Definitely abuse of trust by Verisign
  Site Finder was quickly shut down, lawsuits ensued

## Slide 68: Much More to DNS
Caching: when, where, how much, etc.
Other uses for DNS (i.e. DNS hacks)
  Content Delivery Networks (CDNs) – will be detailed later
  Different types of DNS load balancing
  Dynamic DNS (e.g. for mobile hosts)
DNS and botnets
Politics and growth of the DNS system
  Governance
  New TLDs (.xxx, .biz), eliminating TLDs altogether
  Copyright, arbitration, squatting, typo-squatting