## Slide 1: CSCI-351 Data communication and Networks
Lecture 14: Content Delivery Networks
(Over 1 billion served … each day)
The slide is built with the help of Prof. Alan Mislove, Christo Wilson, and David Choffnes's class

## Slide 2: Announcement (1)
To ask for regrading, you must come to office hours (or send me an email for scheduling) with the following in writing:
  Specify the problem(s) you want regraded
  For each problem, explain why the grade is in error
Chart: Score
| 40 | 50 | 60 | 70 | 80 | 90 | 100
The number of the students | 3 | 4 | 5 | 11 | 7 | 1 | 4

## Slide 3: Announcement (2)
Project 3 will be announced today
  Make your team early (until 11/13)
  HTTP Crawling
    One of the essential skills for your future career
      Data-mining, Visualization, Analysis, etc.
      You will be required to construct a simple database
      Will be relatively easy, thus it doesn’t require milestone submission
Score of Project 2 will be announced at the next class (sorry for the delay)
Notes: http://www.wikicfp.com/cfp/data.jsp

## Slide 4: Announcement (3)
Project 4 is about security stuff
  DNS + Security

## Slide 5: Outline
Motivation
CDN basics
Prominent example: Akamai
Notes: Never go under

## Slide 6: Content in today’s Internet
Most flows are HTTP….
  Web is at least 52% of traffic (as of early 2000), however..
HTTP uses TCP, so it will
  Be ACK clocked
  For Web, likely never leave slow start
    QUIC?
Is the Internet designed for this common case?
  Why?

## Slide 7: Evolution of Serving Web Content
In the beginning…
  …there was a single server
  Probably located in a closet
  And it probably served blinking text
Issues with this model
  Site reliability
    Unplugging cable, hardware failure, natural disaster
  Scalability
    Flash crowds (aka Slashdotting)

## Slide 8: Replicated Web service
Use multiple servers
Advantages
  Better scalability
  Better reliability
Disadvantages
  How do you decide which server to use?
  How to do synchronize state among servers?

## Slide 9: Load Balancers
Device that multiplexes requests across a collection of servers
  All servers share one public IP
  Balancer transparently directs requests to different servers
How should the balancer assign clients to servers?
  Random / round-robin
    When is this a good idea?
  Load-based
    When might this fail?
Challenges
  Scalability (must support traffic for n hosts)
  State (must keep track of previous decisions)

## Slide 10: Load balancing: Are we done?
Advantages
  Allows scaling of hardware independent of IPs
  Relatively easy to maintain
Disadvantages
  Expensive
  Still a single point of failure
  Location!
Where do we place the load balancer for Wikipedia?

## Slide 11: Popping up: HTTP performance
For Web pages
  RTT matters most
  Where should the server go?
For video
  Available bandwidth matters most
  Where should the server go?
Is there one location that is best for everyone?

## Slide 12: Server placement

## Slide 13: Why speed matters
Impact on user experience
  Users navigating away from pages
  Video startup delay

## Slide 14: Why speed matters
Impact on user experience
  Users navigating away from pages
  Video startup delay
Impact on revenue
  Amazon: increased revenue 1% for every 100ms reduction in PLT*
Ping from ROC to LAX: ~100ms
Notes: Demystifying Page Load Performance with WProf - Computer Science ...
https://homes.cs.washington.edu/~arvind/papers/wprof.pdf

## Slide 15: Strawman solution: Web caches
ISP uses a middlebox that caches Web content
  Better performance – content is closer to users
  Lower cost – content traverses network boundary once
  Does this solve the problem?
No!
  Size of all Web content is too large
    Zipf distribution limits cache hit rate
  Web content is dynamic and customized
    Can’t cache banking content
    What does it mean to cache search results?
Notes: Zipf’s law: the frequency of an item is inversely proportional to its rank in a frequency table.

## Slide 16: Outline
Motivation
CDN basics
Prominent example: Akamai

## Slide 17: What is a CDN?
Content Delivery Network
  Also sometimes called Content Distribution Network
  At least half of the world’s bits are delivered by a CDN
    Probably closer to 80/90%
Primary Goals
  Create replicas of content throughout the Internet
  Ensure that replicas are always available
  Directly clients to replicas that will give good performance

## Slide 18: Key Components of a CDN
Distributed servers
  Usually located inside of other ISPs
    Why?
High-speed network connecting them
Clients
  Can be located anywhere in the world
  They want fast Web performance
Glue
  Something that binds clients to “nearby” replica servers

## Slide 19: Key CDN Components
16

## Slide 20: Examples of CDNs
Akamai
  147K+ servers, 1200+ networks, 92 countries (in early 2010)
  240K+ servers, 1700+ networks, 130 countries (now)
Cloudflare, Limelight, Edgecast, and others web service providers (e.g., Google, Facebook)
  Advice…?

## Slide 21: Inside a CDN
Servers are deployed in clusters for reliability
  Some may be offline
    Could be due to failure
    Also could be “suspended” (e.g., to save power or for upgrade)
Could be multiple clusters per location (e.g., in multiple racks)
Server locations
  Well-connected points of presence (PoPs)
  Inside of ISPs

## Slide 22: Mapping clients to servers (1)
CDNs need a way to send clients to the “best” server
  The best server can change over time
  And this depends on client location, network conditions, server load, …
  What existing technology can we use for this?
URL Rewriting
  Modifies the URL of specific content
  netflix.com/movie1 to a17.akamai.com/movie1
  Requires content modification in the origin websites
    But it allows fine-grained controls

## Slide 23: Mapping clients to servers (2)
DNS-based redirection (most widely used)
  DNS Server approaches
    Clients request www.foo.com
    DNS server directs client to one or more IPs based on request IP
    Use short TTL to limit the effect of caching
  CNAME approaches
    Clients request www.foo.com
    Returned record is foo.com CNAME a18.akamai.com

## Slide 24: CDN redirection example
tijay$ dig www.fox.com
;; ANSWER SECTION:
www.fox.com. 510 IN CNAME www.fox-rma.com.edgesuite.net.
www.fox-rma.com.edgesuite.net. 5139 IN CNAME a2047.w7.akamai.net.
a2047.w7.akamai.net. 4 IN A 23.62.96.128
a2047.w7.akamai.net. 4 IN A 23.62.96.144
a2047.w7.akamai.net. 4 IN A 23.62.96.193
a2047.w7.akamai.net. 4 IN A 23.62.96.162
a2047.w7.akamai.net. 4 IN A 23.62.96.185
a2047.w7.akamai.net. 4 IN A 23.62.96.154
a2047.w7.akamai.net. 4 IN A 23.62.96.169
a2047.w7.akamai.net. 4 IN A 23.62.96.152
a2047.w7.akamai.net. 4 IN A 23.62.96.186

## Slide 25: DNS Redirection Considerations
Advantages
  Uses existing, scalable DNS infrastructure
  URLs can stay essentially the same
  TTLs can control “freshness”
Limitations
  DNS servers see only the DNS server IP
    Assumes that client and DNS server are close. Is this accurate?
  Content owner must give up control
  Unicast addresses can limit reliability; the client will connect to “one” IP
Notes: EDNS0 client subnet (Extension DNS)

## Slide 26: CDN Using Anycast
Anycast address
  An IP address in a prefix announced from multiple locations
AS 1
AS 31
AS 41
AS 32
AS 3
AS 20
AS 2
120.10.0.0/16
120.10.0.0/16
?

## Slide 27: Anycasting Considerations
Why do anycast?
  Simplifies network management
    Replica servers can be in the same network domain
  Uses best BGP path
Disadvantages
  BGP path may not be optimal
  Stateful services can be complicated

## Slide 28: Optimizing Performance
Key goal Send clients to server with best end-to-end performance
Performance depends on
  Server load
  Content at that server
  Network conditions
Optimizing for server load
  Load balancing, monitoring at servers
  Generally solved

## Slide 29: Optimizing performance: caching
Where to cache content?
  Popularity of Web objects is Zipf-like
    Also called heavy-tailed and power law
  Nr ~ r-1
  Small number of sites cover large fraction of requests
  Different popularity depending on the location
    Temporal and spatial popularity
  Do you think it is easy to predict?

## Slide 30: Optimizing performance: Network
There are good solutions to server load and content
  What about network performance?
Key challenges for network performance
  Measuring paths is hard
    Traceroute gives us only the forward path
    Shortest path != best path
  RTT estimation is hard
    Variable network conditions
    May not represent end-to-end performance
  No access to client-perceived performance

## Slide 31: Optimizing performance: Network
Example approximation strategies
  Geographic mapping
    Internet paths do not take shortest distance
  Active measurement
    Ping from all replicas to all routable prefixes
    56B * 100 servers * 500k prefixes = 500+MB of traffic per round
  Passive measurement
    Send fraction of clients to different servers, observe performance
    Downside: Some clients get bad performance

## Slide 33: Announcement (1)
Project3
  “SQLite3” is installed on the glados
  You do not need to use virtualenv
Project4 will be announced before the project3
  To give you enough time to implement

## Slide 34: Announcement (2)
Chart: 
Project 1 and 2 Scores | 0.371 | 0.371 | 0.516 | 0.79 | 0.79 | 0.865 | 0.865 | 0.865 | 0.92 | 0.92 | 0.935 | 0.935 | 0.965 | 0.965 | 0.975 | 0.975 | 1 | 1 | 1.03 | 1.03 | 1.04 | 1.04 | 1.05 | 1.05 | 1.05 | 1.05 | 1.075 | 1.075 | 1.15 | 1.15 | 1.15 | 1.15 | 1.15 | 1.15
Chart: Scores (1.0 is the full score)
| Untitled 1 | Untitled 2 | Untitled 3 | Untitled 4 | Untitled 5 | Untitled 6 | Untitled 7 | Untitled 8 | Untitled 9 | Untitled 10 | Untitled 11 | Untitled 12 | Untitled 13 | Untitled 14 | Untitled 15 | Untitled 16 | Untitled 17 | Untitled 18 | Untitled 19 | Untitled 20 | Untitled 21 | Untitled 22 | Untitled 23 | Untitled 24 | Untitled 25 | Untitled 26 | Untitled 27 | Untitled 28 | Untitled 29 | Untitled 30 | Untitled 31 | Untitled 32 | Untitled 33 | Untitled 34
Untitled 1 | 0.075 | 0.075 | 0.168 | 0.168 | 0.2 | 0.2 | 0.495 | 0.495 | 0.55 | 0.55 | 0.5625 | 0.5625 | 0.775 | 0.775 | 0.8 | 0.8325 | 0.85 | 0.85 | 0.91575 | 0.91575 | 1 | 1 | 1.0835 | 1.0835 | 1.0917 | 1.0917 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1 | 1.1
Student’s anonymous ID

## Slide 35: Distribution — Midterm
Chart: 
Midterm Scores | 0.48 | 0.498 | 0.52 | 0.544 | 0.544 | 0.597 | 0.62 | 0.634 | 0.64 | 0.662 | 0.667 | 0.714 | 0.715 | 0.74 | 0.744 | 0.749 | 0.754 | 0.754 | 0.78 | 0.79 | 0.794 | 0.795 | 0.8 | 0.809 | 0.809 | 0.81 | 0.86 | 0.864 | 0.87 | 0.904 | 1.002 | 1.05 | 1.115 | 1.19

## Slide 36: Distribution — Quizzes
Chart: 
All Quizzes scores | 0 | 0.068966 | 0.068966 | 0.10345 | 0.10345 | 0.17241 | 0.22414 | 0.24138 | 0.26207 | 0.27035 | 0.2931 | 0.3069 | 0.32759 | 0.34483 | 0.34483 | 0.37241 | 0.39655 | 0.41379 | 0.43103 | 0.48276 | 0.51724 | 0.53448 | 0.53448 | 0.55172 | 0.56345 | 0.58621 | 0.6069 | 0.60897 | 0.62069 | 0.63793 | 0.68966 | 0.71517 | 0.84483 | 0.92414
This can be higher depending on the result of the rest of the quizzes

## Slide 37: Distributions – potential grades?
Assuming that you would get full scores for all the rest of the projects and exams
  Bonus points and potential quizzes are not taken into account
Chart: 
grades | 0.69947 | 0.72872 | 0.74646 | 0.75955 | 0.76316 | 0.77371 | 0.79416 | 0.7953 | 0.79896 | 0.82156 | 0.8288 | 0.846 | 0.85302 | 0.85525 | 0.85713 | 0.85779 | 0.86014 | 0.86055 | 0.88109 | 0.8816 | 0.88446 | 0.88544 | 0.89323 | 0.90974 | 0.91506 | 0.91636 | 0.91667 | 0.91952 | 0.9253 | 0.9458 | 0.95497 | 0.96343 | 0.99028 | 1.0104
A, A-
B, B-
C, C-

## Slide 38: How to understand CDNs
Deploy multiple servers across the globe
  How to make users connect the CDN server?
    Changing all URLs of the content
    DNS Authoritative server
  How to find the best server?
    IPs of DNS resolver
    Anycast
    EDNS (not covered from the class)

## Slide 39: Outline
Motivation
CDN basics
Prominent example: Akamai

## Slide 40: Akamai case study
Deployment
  147K+ servers, 1200+ networks, 650+ cities, 92 countries
  highly hierarchical, caching depends on popularity
  4 yr depreciation of servers
  Many servers inside ISPs, who are thrilled to have them
  Deployed inside100 new networks in last few years
Customers
  250K+ domains: all top 60 eCommerce sites, all top 30 M&E companies, 9 of 10 to banks, 13 of top 15 auto manufacturers
Overall stats
  5+ terabits/second, 30+ million hits/second, 2+ trillion deliveries/day, 100+ PB/day, 10+ million concurrent streams
  15-30% of Web traffic

## Slide 41: Somewhat old network map

## Slide 42: DNS Redirection
Web client’s request redirected to ‘close’ by server
  Client gets web site’s DNS CNAME entry with domain name in CDN network
  Hierarchy of CDN’s DNS servers direct client to 2 nearby servers
Internet
Web client
Hierarchy of CDN DNS servers
Customer DNS servers
(1)
(2)
(3)
(4)
(5)
(6)
LDNS
Client requests translation for yahoo
Client gets CNAME entry with domain name in Akamai
Client is given 2 nearby web replica servers (fault tolerance)
Web replica servers
Multiple redirections to find nearby edge servers